PEDESTAL RUN
1. Check disk space >500 GB free
2. Check gas set-up:
  1. Open Exit line.
  2. Open exit flow meter.
  3. Check mini gas line connections to GEMs in MTS.
  4. > 2 kPa pressure in gas cylinder
  5. 20 (mL/min) flow
  6. <= 500 ppm O2
3. Check MTS cabling:
  1. Scintillators (SCNL)
    1. SCNL to Switchbox 1 voltage splitter – 3.5 mm cable
    2. SCNL to Quarknet DAQ board – BNC
    3. Quarknet DAQ board to 128L Linear Fan-out 'Input B' – Mini-BNC (cable 74)
    4. 128L Linear Fan-out 'Output B' to Quad CFD input – Mini-BNC
    5. Quad CFD 'Output' to 128L Linear Fan-out 'Input A'
    6. 128L Linear Fan-out 'Output A' to FECs (six (6) total to each FEC)
  2. GEM Detectors
    1. APVs to FECs - HDMI
  3. CAEN Power Supply
    1. CAEN to HV Splitter – BNC (black)
    2. HV Splitter to Detectors – BNC (red)
4. FECs
  1. Ethernet to NETGEAR switches
  2. NETGEAR switches to Date PC Ethernet cards
5. Check voltages (TWO-MAN RULE: Two people shall be present for all high voltage use)
  1. from terminal:
    1. >sudo minicom
    2. >regular pass
    3. >caen
    4. Make sure all parameter are visible
    5. Set all parameters to CONFIG 1 PED “CAEN Power Limit Configs” “tab of MTS_RunInfo_2017.ods”
    6. Press SPACE bar to ramp up each channel (LISTEN FOR SPARKING AND KILL AT CAEN SOURCE IF HEARD)
6. DATE set-up
  1. Ping FECs
    1. >ping FECIPS per “FEC Info” tab of “tab of MTS_RunInfo_2017.ods”
    2. (if needed) power cycle and run >sudo ./ethernet_init.sh from /home/MTSUser/
    3. Start DATE with > ./date.sh from /home/MTSUser/
  2. date
1. Open new Terminal
2. >./date.sh
3. Click lock to take control (buttons should unlock)
4. [<][>] click the right arrow collected data
5. Click “Define” under Define runparameters
6. Click LDC

  1. Make sure the filename is changed from previous run otherwise it will be OVERWRITTEN. // sidenote: when max numebr of subevents = 0, a data run will run forever.
2. [<][>] click the right arrow. Should see two squares turn green. // optional >editDB to see DAQ/FEC IP-ing